## Slide 1: 16.2 IP Addressing Scheme

## Slide 2: * Protocol
ROADMAP
TCP/IP
IPv4 Address
IP Address Types
NAT

## Slide 3: PROTOCOL
Protocol: set of rules to follow to have proper communication.
Network protocols:
TCP/IP - DOD
IPx/SPx - Novell
AppleTalk - Apple
NetBIOS - Microsoft
OSI – ISO

## Slide 4: WHAT IS TCP/IP ?
TCP/IP is a standard protocol used between computers and network devicesfor
communication.
TCP/IP addressing:
IPAddress is logical address given to each and every device in the network.
It is a Network layer address(Layer 3)
Two versions of IP:
  IP Version 4
  IP Version 6

## Slide 5: IPV4 ADDRESS
Bit is represented by 0 or 1.
IP address in binary form (32 bit).
32 bits divided into 4 octets
IP Address
00000000000000000000000000000000
11111111111111111111111111111111
10101010111100000000111111001100
First Octet | Second Octet | Third Octet | Fourth Octet
10101010 | 11110000 | 00001111 | 01010101
8 Bits | 8 Bits | 8 Bits | 8 Bits

## Slide 6: BINARY TO DECIMAL
Taking example as all 0’s
BINARY TO DECIMAL CONVERSION |  |  |  |  |  |  | 
1 | 0 | 1 | 0 | 1 | 0 | 1 | 0
x | x | x | x | X | x | x | x
27 | 26 | 25 | 24 | 23 | 22 | 21 | 20
= | = | = | = | = | = | = | =
128 | 0 | 32 | 0 | 8 | 0 | 2 | 0
128+0+32+0+8+0+2+0=170 |  |  |  |  |  |  | 
170 |  |  |  |  |  |  | 

## Slide 7: BINARY TO DECIMAL ON 4 OCTETS Taking example as all 0’s
BINARY TO DECIMAL CONVERSION |  |  |  |  |  |  |  | BINARY TO DECIMAL CONVERSION |  |  |  |  |  |  |  | BINARY TO DECIMAL CONVERSION |  |  |  |  |  |  |  | BINARY TO DECIMAL CONVERSION |  |  |  |  |  |  | 
1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1
x | x | x | x | x | x | x | x | x | x | x | x | x | x | x | x | x | x | x | x | x | x | x | x | x | x | x | x | x | x | x | x
27 | 26 | 25 | 24 | 23 | 22 | 21 | 20 | 27 | 26 | 25 | 24 | 23 | 22 | 21 | 20 | 27 | 26 | 25 | 24 | 23 | 22 | 21 | 20 | 27 | 26 | 25 | 24 | 23 | 22 | 21 | 20
= | = | = | = | = | = | = | = | = | = | = | = | = | = | = | = | = | = | = | = | = | = | = | = | = | = | = | = | = | = | = | =
128 | 0 | 32 | 0 | 8 | 0 | 2 | 0 | 128 | 64 | 32 | 16 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 8 | 4 | 2 | 1 | 0 | 64 | 0 | 16 | 0 | 4 | 0 | 1
128+0+32+0+8+0+2+0=170 |  |  |  |  |  |  |  | 128+64+32+16+0+0+0+0=240 |  |  |  |  |  |  |  | 0+0+0+0+8+4+2+1=15 |  |  |  |  |  |  |  | 0+64+0+16+0+4+0+1=85 |  |  |  |  |  |  | 
170 |  |  |  |  |  |  |  | 240 |  |  |  |  |  |  |  | 15 |  |  |  |  |  |  |  | 85 |  |  |  |  |  |  | 
IP ADDRESS: 170.240.15.85

## Slide 8: IPV4 Address
IP Address in decimal form: 170.240.15.85
Octets | First Octet | Second Octet | Third Octet | Fourth Octet
Binary | 10101010 | 11110000 | 1111 | 1010101
Decimal | 170 | 240 | 15 | 85
IPADDRESS | 170.240.15.85 |  |  | 

## Slide 9: RANGE OF IPv4 ADDRESS
Taking example as all 0’s
BINARY TO DECIMAL CONVERSION |  |  |  |  |  |  | 
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
x | x | x | x | x | x | x | x
27 | 26 | 25 | 24 | 23 | 22 | 21 | 20
= | = | = | = | = | = | = | =
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0+0+0+0+0+0+0+0=0 |  |  |  |  |  |  | 
0 |  |  |  |  |  |  | 

## Slide 10: RANGE OF IPv4 ADDRESS
Taking example as all 1’s
BINARY TO DECIMAL CONVERSION |  |  |  |  |  |  | 
1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
x | x | x | x | x | x | x | x
27 | 26 | 25 | 24 | 23 | 22 | 21 | 20
= | = | = | = | = | = | = | =
128 | 64 | 32 | 16 | 8 | 4 | 2 | 1
128+64+32+16+8+4+2+1=255 |  |  |  |  |  |  | 
255 |  |  |  |  |  |  | 

## Slide 11: RANGE OF IPv4 ADDRESS
www.cognixia.com
Taking example as all 1’s in all four octets
BINARY TO DECIMAL CONVERSION |  |  |  |  |  |  |  | BINARY TO DECIMAL CONVERSION |  |  |  |  |  |  |  | BINARY TO DECIMAL CONVERSION |  |  |  |  |  |  |  | BINARY TO DECIMAL CONVERSION |  |  |  |  |  |  | 
1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
x | x | x | x | x | x | x | x | x | x | x | x | x | x | x | x | x | x | x | x | x | x | x | x | x | x | x | x | x | x | x | x
27 | 26 | 25 | 24 | 23 | 22 | 21 | 20 | 27 | 26 | 25 | 24 | 23 | 22 | 21 | 20 | 27 | 26 | 25 | 24 | 23 | 22 | 21 | 20 | 27 | 26 | 25 | 24 | 23 | 22 | 21 | 20
= | = | = | = | = | = | = | = | = | = | = | = | = | = | = | = | = | = | = | = | = | = | = | = | = | = | = | = | = | = | = | =
12 8 | 64 | 32 | 16 | 8 | 4 | 2 | 1 | 12 8 | 64 | 32 | 16 | 8 | 4 | 2 | 1 | 12 8 | 64 | 32 | 16 | 8 | 4 | 2 | 1 | 12 8 | 64 | 32 | 16 | 8 | 4 | 2 | 1
128+64+32+16+8+4+2+1=255 |  |  |  |  |  |  |  | 128+64+32+16+8+4+2+1=255 |  |  |  |  |  |  |  | 128+64+32+16+8+4+2+1=255 |  |  |  |  |  |  |  | 128+64+32+16+8+4+2+1=255 |  |  |  |  |  |  | 
255 |  |  |  |  |  |  |  | 255 |  |  |  |  |  |  |  | 255 |  |  |  |  |  |  |  | 255 |  |  |  |  |  |  | 
255 |  |  |  |  |  |  |  | 255 |  |  |  |  |  |  |  | 255 |  |  |  |  |  |  |  | 255 |  |  |  |  |  |  | 
255.255.255.255 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 

## Slide 12: RANGE OF IPv4 ADDRESS
Total IP Address Range: 0.0.0.0 to 255.255.255.255
MIN | 0 | 0 | 0 | 0
MAX | 255 | 255 | 255 | 255

## Slide 13: IP ADDRESS CLASSIFICATION
IP ADDRESS are divided into 5 classes
CLASS A, B, C used in LAN & WAN
CLASS D reserved for multicasting
CLASS E reserved for research & development and for future use
CLASS NAME | STARTING IP | ENDING IP
CLASS A | 0.0.0.0 | 127.255.255.255
CLASS B | 128.0.0.0 | 191.255.255.255
CLASS C | 192.0.0.0 | 223.255.255.255
CLASS D | 224.0.0.0 | 239.255.255.255
CLASS E | 240.0.0.0 | 255.255.255.255

## Slide 14: TYPES OF COMMUNICATION
In an IPv4 network, the hosts can communicate one of three differentways:
Unicast
Broadcast
Multicast
One to One
One to All
One to Many

## Slide 15: DIFFERENCE BETWEEN PUBLIC AND PRIVATE IP
PUBLIC IP | PRIVATE IP
Used on public network(INTERNET) | Used with the LAN or within the organization
Recognized on internet | Not recognized on internet
Given by the service provider(from IANA) | Given by the administrator
Globally unique | Unique within the network or organization
Pay to service provider | Free
Registered | Unregistered IP

## Slide 16: PRIVATE IP ADDRESS
There are certain addresses in each class of IP address that are reserved for Private Networks.
These addresses are called private addresses.
CLASS | START IP | END IP
CLASS A | 10.0.0.0 | 10.255.255.255
CLASS B | 172.16.0.0 | 172.31.255.255
CLASS C | 192.168.0.0 | 192.168.255.255

## Slide 17: ELASTIC IP ADDRESS
To use an Elastic IP address, you first allocate one to your account, andthen
associate it with your instance or a network interface.
When you associate an Elastic IP address with an instance or its primary network interface, the instance's public IP address (if it had one) is released back into Amazon's pool of public IP addresses.
You can disassociate an Elastic IP address from a resource, and reassociate it with a different resource.
A disassociated Elastic IP address remains allocated to your account until you
explicitly release it.
An Elastic IP address is for use in a specific region only.

## Slide 18: NETWORK AND HOST PORTIONS
IP Address is divided into Network & HostPortion.
Host: specific a device in the network. Network: set of devices
CLASS | NETWORK/HOST PORTION
CLASS A | N.H.H.H
CLASS B | N.N.H.H
CLASS C | N.N.N.H

## Slide 19: SUBNET MASK
CLASS A DEFAULT SUBNET MASK 255.0.0.0 |  |  |  | 
/ 8 | N | H | H | H
 | 255 | 0 | 0 | 0
 | 11111111 | 00000000 | 00000000 | 00000000
CLASS B DEFAULT SUBNET MASK 255.255.0.0 |  |  |  | 
/16 | N | N | H | H
 | 255 | 255 | 0 | 0
 | 11111111 | 11111111 | 0 | 0
CLASS C DEFAULT SUBNET MASK 255.255.255.0 |  |  |  | 
/24 | N | N | N | H
 | 255 | 255 | 255 | 0
 | 11111111 | 11111111 | 11111111 | 0

## Slide 20: NETWORK ADDRESS TRANSLATION (NAT)
www.cognixia.com
NAT (Network Address Translation) Maps Private IPs to Public IPs It is required because of shortage of IPv4 Address
You can use a network address translation (NAT) instance in a public subnet in your VPC to enable instances in the private subnet to initiate outbound IPv4 traffic to the Internet or other AWS services, but prevent the instances from receiving inbound traffic initiated by someone on the Internet.

## Slide 21: NETWORK ADDRESS TRANSLATION (NAT)

## Slide 22: THANK YOU